This is a board to adapt a 2.4Ghz Ebyte E28 lora module into a breadboard friendly format.
The board will allow you to use the Ebyte E28 with a standard 0.1” matrix breadbord or stripboard.
The Ebyte E28 module uses a PCB antenna, no external antenna is needed. The boards are supplied with the 0.1" pins unsoldered, leaving you the option of how to assemble or use the board in a project.
The Ebyte E28-2G4M20S module has RX and TX enable pins, these are connected on this board and need to be switched accordingly.

This board can be used with the Easy mikroBUS™ Pro Mini controller available in this shop.

Do not operate the Ebyte E28 device without an antenna. The Ebyte E28 is a 3.3V supply and 3.3V logic level device, do not use directly with 5V controller boards such as the Arduino UNO.
The pinout of the board is below, the lora device pins on the outside.

There are many examples for using these boards for GPS trackers or sensors provided in an Arduino the library here; https://github.com/StuartsProjects/SX12XX-LoRa